## Slide 1: Microscopy imaging

## Slide 2: Standard microscope
1. Eyepiece (ocular lens)
2. Objective turret to hold multiple objective lenses
3. Objective lenses
4. Focus knobs (to move the stage), coarse
5. Focus knobs, fine adjustment
6. Stage (to hold the specimen)
7. Light source (a light or a mirror)
8. Diaphragm and condenser
9. Mechanical stage

## Slide 3: Transillumination
NA = n sin()

## Slide 4: Inverted microscope

## Slide 5: Imaging with fluorescence
The sample contains one or more fluorescent substances – fluorophores
Each fluorophore emits light at a specific waveband when stimulated (excited) by light at a different, lower, wavelength

## Slide 6: Principle of Fluorescence
Energy is absorbed by the atom which becomes excited.
The electron jumps to a higher energy level.
Soon, the electron drops back to the ground state, emitting a photon (or a packet of light) - the atom is fluorescing.
http://www.nobelprize.org/educational/physics/microscopes/fluorescence/

## Slide 7: Principle of Fluorescence
Both absorption and emission wavebands are unique for a particular molecular structure of a fluorophore.
The difference between the absorption and the emission peak is called Stokes shift.
Fluorescence efficiency (quantum yield) is the ratio of the number of photons emitted to the number of photons absorbed

## Slide 8: Fluorescence microscope

## Slide 9: Fluorescence microscope
Light source is filtered to let through only the excitation waveband
Excitation light illuminates the specimen
Emission light (much weaker than excitation light) is re-emitted from the specimen
The second filter lets through only the emission waveband
This light is then recorded by the microscope’s camera

## Slide 10: Dichroic (beamsplitter) mirror
Excitation filter
Dichroic mirror
Emission filter

## Slide 11: Applications of fluorescence microscopy
Fluorescence microscopy has revolutionised biomedical sciences (Nobel Prize!)
Hundreds of fluorescent compounds have been created by chemists, including synthetic nano-beads
Used as markers that can be attached to various very specific cellular and sub-cellular structures, proteins and compounds of interest
Used to study biological systems is vitro and in vivo

## Slide 12: Fluorescence Microscopy
Osamu Shimomura, Martin Chalfie and Roger Tsien,
Nobel Prize for Chemistry, 2008
Osamu Shimomura, Professor Emeritus at Marine Biological Laboratory (MBL) in Woods Hole, Massachusetts was awarded the Nobel Prize in Chemistry in 2008 for the discovery and development of green fluorescent protein (GFP) with two American scientists: Martin Chalfie of Columbia University and Roger Tsien of the University of California-San Diego. They were jointly awarded for discovering the green fluorescent protein (GFP) and further development for use in cell biology. By fluorescence of GFP, the spatial and temporal distribution of other proteins in living cells, tissues or organisms can be observed directly, thus laying the foundation for modern fluorescence microscopy.

## Slide 13: Epifluorescence microscopy
The entire sample is illuminated

## Slide 14: Confocal microscopy
Only a thin layer of the sample is illuminated

## Slide 15: Epiluminescence vs confocal microscopy

## Slide 16: TIRF microscopy
TIRF = Total Internal Reflection Fluorescence
100 nm

## Slide 17: Epiluminescent vs TIRF Microscopy

## Slide 18: Multifluorescence microscopy
Imaging several compounds simultaneously

## Slide 19: Challenges in multifluorescence microscopy
Different fluorophores require different filter sets
Fluorophores are bleached by light
Live cells exhibit motion
Cell bodies emit very broad-band background fluorescence

## Slide 20: Challenges in multifluorescence microscopy

## Slide 21: Challenges in multifluorescence microscopy
We can unmix emissions after image acquisition

## Slide 22: Spectral unmixing

## Slide 23: Spectral unmixing
A method for isolating contributions of the individual fluorophores from their mixture
Normally requires the knowledge of the emission spectra of the fluorophores
Assumption: the combined emission is a linear combination of the contributing emissions
Normally requires imaging at a number of spectral wavelengths

## Slide 24: Spectral unmixing
K – the number of wavelengths at which the image was acquired
N – the number of fluorophores
Ln – the emission spectrum of fluorophore n; the length of each spectrum Ln is K
M - the number of samples (pixels in the image). A multispectral image I comprises K×M spectral measurements in total.

## Slide 25: Spectral unmixing
A spectrum s at any given pixel has contributions from N library spectra with a coefficient an describing the relative abundance of Ln:
s = L a
s – a column vector of K spectral measurements
L - K×N matrix of N K-dimensional library spectra Ln
a - N-dimensional column vector of abundance coefficients
If K≥N,
a = L-1 s

## Slide 26: Spectral unmixing examples
Fluorescent beads – testing the method
In mixture
Unmixed

## Slide 27: Cell Fluorescence Studies
Multispectral image
Reference spectra
Linear
Unmixing
Cell Autofluorescence
CFP Fluorescence

## Slide 28: Cancer research
Reference Spectra
Multispectral Image
Linear
Unmixing
Autofluorescence
Quantum Dot Fluorescence

## Slide 29: Other microscopies
FRET (Förster Resonance Energy Transfer)
DIC (Differential Interference Contrast)
Phase Contrast Microscopy
Super-resolution techniques
PALM (Photoactivated Localization Microscopy(PALM))
STORM (Stochastic Optical Reconstruction Microscopy
STED (Stimulated Emission Depletion)
Electron microscopies

## Slide 30: FRET microscopy
Excitation filter
Specimen
Detector
White light source
Emission filter
Dichroic mirror
Ex
DM
R1
R2
FRET = Förster Resonance Energy Transfer

## Slide 31: FRET microscopy
Excitation light stimulates one of the fluorophores
If the second fluorophore has its excitation waveband overlapping with the emission waveband of the first fluorophore, and it is at the same location, it resonates and becomes excited
It emits radiation at its characteristic emission waveband

## Slide 32: FRET microscopy
http://www.embl.de/eamnet/downloads/modules/FRET_teaching_module.pdf

## Slide 33: DIC Microscopy
DIC = Differential Interference Contrast

## Slide 34: DIC Microscopy

## Slide 35: DIC Microscopy
Computing estimates of platelet cell size and thickness