## Slide 1: Digital image processing and analysis 6. Image enhancement: manipulating image frequencies
Professor Ela Claridge
School of Computer Science

## Slide 2: Previous lecture:
Image enhancement and restoration
  Image histogram
  Manipulating image brightness
  Contrast enhancement
  LUT operations

## Slide 3: In this lecture we shall find out about:
Common types of image corruption
  Noise
  Blur
Image frequencies
Tools and methods for noise removal
  Image profile
  Image filtering operations
  Convolution
  Low-pass (smoothing) filters

## Slide 4: Image corruption Causes
An input digital image is never perfect, but is always “noisy” and distorted to some extent.

## Slide 5: Image corruption Causes
An input digital image is never perfect, but is always “noisy” and distorted to some extent by:
  Non-linearities of electronic components of sensors
  Sampling and quantisation errors
  Suboptimal imaging conditions
  Data transmission artefacts
Sensor
Potential
well
Amplifier
ADC

## Slide 6: Image corruption Noise and blur
Uncorrupted image
Image corrupted by noise
Image corrupted by blur

## Slide 7: Frequency Image profile
Image profile

## Slide 8: Frequency Image profile
Low frequency
Low
High
High

## Slide 9: Frequency Image profile
Uncorrupted image
Image corrupted by noise
Image corrupted by blur
Image profiles
Higher frequency
Lower frequency

## Slide 10: Frequency Image profile

## Slide 11: Frequency filtering operations Tool for reducing frequency distortions
Frequency filtering operations separate frequency components within an image into different frequency ranges, most often into:
  low frequency components
  high frequency components
Following this separation
  unwanted components can be rejected or,
  low and high frequency components can be processed separately and then re-combined.

## Slide 12: Frequency filtering operations Smoothing: low pass filter
One of the simplest methods to remove noise is to average the incoming signal over the number of sensors.
The spatial averaging produces visually smoother image; this is because the unwanted high frequencies are eliminated by averaging.
This process of smoothing works by removing rapid changes in brightness (high frequency component) but at the same time retaining slow changes (low frequency component).
Averaging of pixel values is an example of a simple digital image processing technique for reducing high frequency component of an image.

## Slide 13: Frequency filtering operations Smoothing: low pass filter
To smooth the image, for every pixel in the original image the average pixel value is calculated for 3x3 pixel area of the image
(here pixels p1 – p9) and inserted in the position of the original pixel in a new image (here at the location of pixel p5).
 | New pixel value | 
new pixel value

## Slide 14: Frequency filtering operations Smoothing: low pass filter
This is equivalent to multiplying pixel values p1 - p9 by values stored in a small 3x3 matrix called a convolution kernel (or a convolution mask or a filter).
A convolution kernel can also be thought of as a set of spatial weights applied to an input signal.
new pixel value
p1 | p2 | p3
p4 | p5 | p6
p7 | p8 | p9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9

## Slide 15: Frequency filtering operations Convolution
Input image
Resulting output image
Convolution kernel
Active pixel

## Slide 16: Frequency filtering operations Convolution

## Slide 17: Frequency filtering operations Convolution

## Slide 18: Frequency filtering operations Convolution

## Slide 19: Frequency filtering operations Convolution
Convolution is a very important image processing operation. It is an example of a so-called linear transformation because the only operations necessary are that of addition and multiplication.
Depending on the weights in the kernel, many different image processing operations can be carried out using convolution.

## Slide 20: Frequency filtering operations Low-pass filters
Low pass filters remove high frequency components and pass through low frequency components. Most low frequency filters suffer from the side effect: blur.
Uncorrupted image
Image corrupted by noise
Image restored by low-pass filtering

## Slide 21: Frequency filtering operations Low-pass filters
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/10 | 1/10 | 1/10
1/10 | 1/5 | 1/10
1/10 | 1/10 | 1/10
1/16 | 1/8 | 1/16
1/8 | 1/4 | 1/8
1/16 | 1/8 | 1/16
Examples of low pass filters
Can you deduce the principles?

## Slide 22: Frequency filtering operations Low-pass filters
k1 | k2 | k3
k4 | k5 | k6
k7 | k8 | k9
Can you deduce the principles?
k1+k2+ … +k9 = 1
0 ≤ ki < 1
kcentre ³ remaining ki

## Slide 23: Frequency filtering operations Low-pass filters
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/9 | 1/9 | 1/9
1/10 | 1/10 | 1/10
1/10 | 1/5 | 1/10
1/10 | 1/10 | 1/10
1/16 | 1/8 | 1/16
1/8 | 1/4 | 1/8
1/16 | 1/8 | 1/16
Examples of low pass filters (again)

## Slide 24: Frequency filtering operations Low-pass filters
Can you deduce the principles?
Intuitive hints
If all pixels in a small image region have the same value, the result of convolution is that constant value.
The same image values => frequency 0 (lowest), so “passed through” a low-pass filter
If pixel values in a small image region change rapidly, the result of convolution is the average value over the region.
High frequencies “removed”, only low frequency “base” value passed through.
k1 | k2 | k3
k4 | k5 | k6
k7 | k8 | k9

## Slide 25: Frequency filtering operations Low-pass filters
1/16 | 1/8 | 1/16
1/8 | 1/4 | 1/8
1/16 | 1/8 | 1/16
A typical profile of a low-pass filter

## Slide 26: Frequency filtering operations Low-pass filters: Gaussian smoothing
A two-dimensional Gaussian function makes a flexible smoothing kernel. The formula is:
The amount of smoothing depends on the value of s:
the greater the s the stronger the effect of smoothing.
s = 2.5
s = 5

## Slide 27: Frequency filtering operations Low-pass filters: Gaussian smoothing
s = 2.5
s = 5.0

## Slide 28
Effects of Gaussian smoothing
s = 2.5
s = 5.0

## Slide 29: Frequency filtering operations Low-pass filters
Applications
  Removing visual "noise" present in an image
  Smoothing - removing high frequency components to examine low frequency ones
Side effect: blur

## Slide 30: Frequency filtering operations Low-pass filters in nature
Ganglion cells
Bipolar cells
Horizontal cells

## Slide 31: Frequency filtering operations Low-pass filters in nature
Horizontal cells
Integrate and regulate the input from multiple photoreceptor cells
Retinal receptors
Horizontal cell
Weights
Effect: weighted averaging of inputs

## Slide 32: In this lecture we have covered:
Common types of image corruption
  Noise
  Blur
Image frequencies
Tools and methods for noise removal
  Image profile
  Image filtering operations
  Convolution
  Low-pass (smoothing) filters

## Slide 33: Next lecture:
Causes of image blur
Combining frequencies for image sharpening
Digital filtering for image sharpening
  Sharpening filters
  High-pass filters
How human visual system sharpens images

## Slide 34: Further reading and experimentation
Book chapters:
Sonka, M. Hlavac, V. Boyle, R. Image Processing, Analysis and Machine Vision, Chapman & Hall Computing (various editions), 4.3.1.
Gonzalez, R.C. & Woods, R.E. Digital Image Processing, Addison-Wesley (various editions), 4.2.4, 4.3.2.
Umbaugh, S.E. Computer vision and image processing : a practical approach using CVIPtools , Prentice Hall International (various editions), 3.2, 4.1, 4.2, 4.4.
Image noise: https://photographylife.com/photo-noise-reduction-tutorial
HIPR2 resources
Mean (average) filter: http://homepages.inf.ed.ac.uk/rbf/HIPR2/mean.htm
Gaussian smoothing http://homepages.inf.ed.ac.uk/rbf/HIPR2/gsmooth.htm