## Slide 1: Digital image processing and analysis 15. Multispectral imaging
Professor Ela Claridge
School of Computer Science

## Slide 2: Previous lecture:
Statistical shape models
  What they are
  What they are used for
Principal Component Analysis (PCA)
  What it is
  How it is used for shape modelling
Point distribution models
Active shape models
Active appearance models

## Slide 3: In this lecture we shall find out about:
Multispectral imaging
  Why colour that we see does not always tell the full story
  General principles of multispectral imaging
  How to acquire multispectral images
  Analysis and applications

## Slide 4: What is perception for?
Quantitative imaging may lay beyond our perception

## Slide 5: How bees see the world
https://www.visualnews.com/2013/04/08/hidden-patterns-how-a-bee-sees-the-world-of-flowers/
In the vast electromagnetic spectrum of wavelengths (extending from below the long wavelengths used for radio, to the short wavelengths of gamma radiation) we humans see only a miniscule fraction that we call visible light. This small sliver, spanning the distance between violet and red is the way we perceive the world around us with our eyes. However bees and other insects have a different view of the world. Their whole range of light is shifted further towards the violet end of the spectrum and further from the red. This means that, while they can’t perceive red, they see colours we simply cannot see – what we call ultra-violet. This also means is that bees see a world literally hidden before our eyes.
Human vision
(RGB)
Simulated bee vision
(GB+UV)

## Slide 6: How birds see the world
Human vision
(RGB)
UV vision
(Ultraviolet)
Simulated bird vision
(RGB+UV)

## Slide 7: Light – a form of electromagnetic radiation

## Slide 8: Spectral sensitivity curves for the retinal receptors
Change title
Notes: The cone cells of the human eye are sensitive to 3 wavelength ranges which the eye interprets as blue (narrow, with a peak near 419 nm), green (broader, with a peak near 531 nm) and red (also broad, with a peak near 558 nm, which is actually more like yellow!):

## Slide 9: Spectra of different species vision There are things we (humans) cannot see
Humans
Bees
Birds

## Slide 10: Colour pereception - problems There are things we cannot see

## Slide 11: Colour perception – problems Inability to “unmix”
Inability to “unmix”

## Slide 12: Colour perception – problems Metamerism
580 nm
500 nm
650 nm
580 nm
500 nm
650 nm

## Slide 13: Colour perception – problems Metamerism
Two colours that have different spectra look the same to the human eye.
They will appear differently in different illuminating conditions
Indoors
Outdoors

## Slide 14: Colour perception – problems Colour constancy
In these two pictures, the second card from the left seems to be a stronger shade of pink in the upper one than in the lower one. In fact they are the same colour (since they have the same RGB values), but perception is affected by the colour cast of the surrounding photo.
Source: Wikipedia

## Slide 15: Sensors: limited spectral resolution Both: human eyes and colour cameras
400
500
600
700
l(nm)
S(l)
400
500
600
700
l(nm)
S(l)

## Slide 16: Multispectral and hyperspectral imaging
Reflected, transmitted or emitted light collected by a camera forms an image
Monochrome (B/W) – collects all visible light
Colour – three broad bands (RGB)
Multispectral – several – several tens of bands (broad or narrow)
Hyperspectral – many (hundreds) narrow bands

## Slide 17: Multispectral Imaging RGB – broad-band filters
400
500
600
700
l(nm)
S(l)
400
500
600
700
l(nm)
S(l)
0.6
0.4
0.5
0.6
0.4
0.5
The same RGB image values for different spectral reflectance

## Slide 18: Multispectral Imaging Narrow-band filters
400
500
600
700
l(nm)
S(l)
400
500
600
700
l(nm)
S(l)
0.6
0.7
0.7
0.4
0.3
0.5
0.6
0.8
0.6
0.4
0.4
0.5
0.5
0.5
Different multispectral image values for different spectral reflectance

## Slide 19: Why multispectral imaging? Richer interpretation
Example: spectral reflectance curve of the human skin
450 550 650 nm
Wavelength ()

## Slide 20: Why multispectral imaging?
Full representation of spectral properties
Overcomes problems of human perception
Extends human senses
Monochrome
Multispectral
RGB

## Slide 21: Why multispectral imaging?
Hyperspectral cube
(lambda-stack)
Full representation of spatial properties
Overcomes the lack of spatial information in point spectroscopy
At the same time …
X
Y


## Slide 22: Multispectral image representation
507
525
552
585
611
680

## Slide 23: What’s in the image data?
Contributing factors
  Illumination
  Imaging system
  Object

## Slide 24: What’s in the image data? Different illumination
Spectra of common sources of visible light

## Slide 25: What’s in the image data? Camera sensors

## Slide 26: What’s in the image data? Imaging system filters
A filter is a device which selectively transmits light having a particular range of wavelengths while blocking the remainder

## Slide 27: What’s in the image data? Calibration and normalisation
To correct interpret image data it is necessary to remove the effects of
  Illumination
  Imaging system / filters
  Acquisition time
  Aperture
  ….
Mathematical techniques for doing so are referred to as “calibration” and “normalisation”.

## Slide 28: Acquiring multispectral images
Several ways of obtaining multispectral images
Filter-based devices
  Filter wheels
  Programmable filters
Diffraction-based devices
  Pushbroom imaging
Narrow-band illumination

## Slide 29: Acquiring multispectral images Filter Wheel
object

## Slide 30: Acquiring multispectral images Pushbroom
Scanning one spatial dimension
Spatial x spectral area scan sensor
Prism or diffraction grating to separate wavelength

## Slide 31: Acquiring multispectral images Pushbroom
Source: http://rst.gsfc.nasa.gov/Intro/pushbroomX.jpg
 (spectral)
X (spatial)

## Slide 32: Acquiring multispectral images Programmable Filters
Made of liquid crystal elements.
By switching them on in different combinations, the filter can be configured to pass different wavebands.
Can switch rapidly between bands to duplicate the effect of changing filters in the filter wheel.
One programmable filter can mimic several hundred separate filters.
T1
T3
T5
T4
T6
T2
T1*T2*T3*T4*T5*T6

## Slide 33: Acquiring multispectral images Programmable Filters
QE for VariSpec (C.R.I.) programmable filter

## Slide 34: Acquiring multispectral images Narrow band illumination
Integrating sphere
Uniform, diffuse
illumination
LEDs as light source
Notes: 34

## Slide 35: Multispectral image analysis Measurable properties
Reflectance
Absorption
Emission
Depth of penetration

## Slide 36: Multispectral imaging Applications

## Slide 37: Kinds of applications Visualisation
Proteins interacting
Fluorescence levels imaged through filter centred at 1
Fluorescence at 2
1 mapped to red
2 mapped to green
Where fluorescence is coincident at 1 and 2, we see yellow as superposition of red and green

## Slide 38: Kinds of applications Classification
http://www.space.gc.ca/asc/eng/satellites/hyper_brochure.asp
Library

## Slide 39: Kinds of applications Quantitative analysis
http://biomedicaloptics.spiedigitallibrary.org/data/journals/biomedo/934852/jbo_21_1_016008_f003.png

## Slide 40: Application areas Arts
http://thecreatorsproject.vice.com/blog/how-art-experts-discovered-a-hidden-portrait-beaneath-a-picasso-masterpiece

## Slide 41: Application areas Archeology
http://www.archaeology.org/issues/207-1603/features/4155-egypt-monastery-palimpsests#art_page2
In 1996, a Georgian scholar used ultraviolet light to read a Sinai palimpsest with an overtext in medieval Georgian. He found that the underlying text was written in Caucasian Albanian, and was the first example of a text written in this now-extinct language.

## Slide 42: Application areas Restoration
https://people.rit.edu/andpph/photofile-b/ir-letter-comparison-1.jpg

## Slide 43: Application areas History
http://boingboing.net/2014/06/17/hidden-painting-found-under-pi.html
Multispectral analysis of a document in the Library of Congress revealed that a draft of the Declaration of Independence originally named Americans "subjects" instead of "citizens".

## Slide 44: Application areas Forensics
https://github.com/golanlevin/ExperimentalCapture/blob/master/docs/hyperspectral.md

## Slide 45: Application areas Astronomy
Astronomers use multispectral imaging to understand the Sun.

## Slide 46: Application areas Environment
Google has recently made satellite thermal imaging of roofs available to the public, to prompt people's awareness about the heat inefficiency of their homes.

## Slide 47: Application areas Environment
4-band multispectral imagery.
The infrared band responds to the chlorophyll found in vegetation and allows for the identification and examination of urban tree canopies.
http://www.ayresgeospatial.com/2014/04/18/geospatial-solutions-for-urban-forest-management/

## Slide 48: Application areas Environment
The spectrometer works in conjunction with a laser that fans out beneath the aircraft, creating a 3-D image of the forest below.
By marrying the data from the spectrometer and the laser, topographic images created show the condition of the forest. Healthy trees are blue, and drought-stressed trees run from mild (yellow) to severe (red).

## Slide 49: Application areas Agriculture
Hyperspectral and chlorophyll fluorescence Imaging for early detection of plant diseases, with Special Reference to Fusarium spec. Infections on Wheat
http://www.mdpi.com/2077-0472/4/1/32

## Slide 50: Application areas Agriculture
Healthy and damaged fruit areas show different reflectance spectra.

## Slide 51: Application areas Thermal imaging

## Slide 52: Application areas Medicine
Thermal imaging

## Slide 53: Application areas Medicine
Thermal imaging of the skin burns

## Slide 54: Application areas Quality control
Fusarium detection
Out of range tablet identification
VideometerLab Multispectral Imaging System
http://analytik.co.uk/product/multispectral-imaging-videometerlab-analyser/

## Slide 55: Application areas Security
Millimeter wave and Terahertz imaging
https://github.com/golanlevin/ExperimentalCapture/blob/master/docs/hyperspectral.md

## Slide 56: Research at Birmingham Multispectral imaging for medical diagnosis

## Slide 57: Research at Birmingham Early diagnosis of skin cancer
Collagen
Dermal melanin
Epidermal melanin
Blood
Colour
Preece S and Claridge E (2004) Spectral filter optimisation for the recovery of parameters which describe human skin.
IEEE Trans. PAMI 26(7), 913-922.

## Slide 58: Research at Birmingham Early diagnosis of skin cancer
SIAscopy / MoleMate
Claridge E, Cotton S, Moncrieff M, Hall P (2006) Spectrophotometric Intracutaneous Imaging (SIAscopy): Method and clinical applications. Chapter 37 in Handbook of Non-Invasive Methods and the Skin (2nd ed). Serup J, Jemec GBE, Grove G (Eds), 315-325: CRC Press.

## Slide 59: Research at Birmingham Burns assessment
SIAscopy
Blood perfusion
Pigment damage

## Slide 60: Research at Birmingham Detecting diabetic complications in the eye
Image of retina
Haemoglobin map

## Slide 61: Research at Birmingham Signs of age related macular degeneration
Macular pigment maps
Styles IB, Calcagni A, Claridge E, Orihuela Espina F, Gibson JM (2006) Quantitative analysis of multispectral fundus images.
Medical Image Analysis 10(4), 578-597.

## Slide 62: Research at Birmingham Skin pigment maps
Colour
Haemoglobin
Melanin
http://www.cs.bham.ac.uk/~exc/Research/publications.php
http://www.cs.bham.ac.uk/~exc/Research/projects.php

## Slide 63: In this lecture we have covered:
Multispectral imaging
  Why colour that we see does not always tell the full story
  General principles of multispectral imaging
  How to acquire multispectral images
  Applications

## Slide 64: Next lecture:
Overview and summary of the course
Structure of the exam paper
Revising for the exam

## Slide 65: Further reading and experimentation
Links to the articles and image sources are included in the individual slides, where relevant.